## Slide 1: Drifters, containers and floating objects Cláudia Neto Viegas, Rodrigo Fernandes
MOHID Workshop ARCOPOL- Lisbon,13th October 2011

## Slide 2: Drifters, containers and floating objects
Aims
Methodology (different field works and modelling)
  In Finisterra, open sea (Galicia, Spain)
  In Mondego, River (Portugal)
  In Estoril Coast, estuary and costal zone (Portugal
Main results and model developments
MOHID Drift modelling specifications

## Slide 3: Drifters, containers and floating objects Aims
To develop and improve modelling tools to simulate and predict the fate and behaviour of oil spills, HNS and inerts.
Drifters releases (field work) to validate models.
  Using different drifters, on different areas:
    Floating buoys with diffenrent drogues;
    Popcorns;
Field Work to better know the local hydrodynamic.
Model calibration and developments.

## Slide 4: Drifters, containers and floating objects Different field works and modelling
Field exercise in Galician Coast (Finisterre) with intercomparison of drift model results in relation to the observed trajectory of the buoys. MOHID showing the best modelled trajectory, with a bias of 11%
Notes: In Galicia, and since 2006, several real-time model comparison exercises have been deployed in cooperation with different Institutions (Meteogalicia, Sasemar, Intecmar) and involving different resources (aerial observations, modellers, etc.) using drifter buoys trajectories and analysing the bias between different modelled and observed trajectories. Next figure illustrates an exercise in Finisterre, in November 2006, were MOHID presented the best fit to the observations, with a bias of 11%. The second best model showed a bias of 28%.

## Slide 5: Drifters, containers and floating objects Different field works and modelling
MOHID forecast of popcorn release, in Mondego. Field results followed the same behavior than mohid forecast simulations.
Random behaviour of particles, wind coefficient 0.015
Notes: Foram lançadas pipocas na Foz do Rio MONDEGO. O IST fez no dia anterior ao lançamento a simulação do comportamento das pipocas.
A Universidade de Aveiro confirmou que as pipocas seguiram o percurso simulado pelo MOHID.

## Slide 6: Drifters, containers and floating objects Different field works and modelling
MOHID forecast of popcorn release, in Mondego. Field results followed the same behavior than mohid forecast simulations.
Random behaviour of particles, wind coefficient 0.03
Notes: Foram lançadas pipocas na Foz do Rio MONDEGO. O IST fez no dia anterior ao lançamento a simulação do comportamento das pipocas.
A Universidade de Aveiro confirmou que as pipocas seguiram o percurso simulado pelo MOHID.

## Slide 7: Drifters, containers and floating objects Field works in Estoril Coast
Aims:
  Model calibration and validation for Estoril Coast;
  Implementation of a semi-operational oil spill fate and behaviour modelling system in Estoril Coast;
  Buoys release, follow their trajectory and compare field results with model simulations.
  To better know local hydrodynamic and behaviours.
Notes: O trabalho de campo na Costa do Estoril, teve como principais objectivos: a calibração do modelo para o local. A implementação de um modelo semi operacinal, de forma a poder fazer várias simulações quase me tempo real.
O lançamento de bóias e a monitorização e registo das suas trajectórias, de forma a comparar os resultados de campo com os resultados do modelo.
Foram planeadas campanhas com o lançamento de bóias em diferentes pontos da costa do estoril, em diferentes condições de maré e vento, de forma a melhor conhecer melhor as condições locais, as recirculações e características próprias da embocadura do Tejo e das correntes junto à linha de costa.

## Slide 8
Study area : Estoril Coast (Lisbon – Parede)
  Estoril Coast:
    Tagus river influence;
    Atlantic Ocean influence;
    Several Bathing Waters;
    Lisbon Harbour entrance;
    Fishing area.
Drifters, containers and floating objects Field works in Estoril Coast
Notes: A Costa do Estoril, é fortamente influenciada pela descarga do Rio Tejo.
Mas também pela dinâmica das marés.
A linha de costa é bastante recortada e contém várias baías e praias, que contribuem para a criação de campos hidrodinâimcos característicos, com ocorrência de pequenas recirculações, e a possibilidade de materiais ficarem retido junto à linha de costa.
A circulação de embarcações é intensa, quer pela entrada e saída de grandes embarcações do Porto de Lisboa, quer peo facto de ser uma zona piscatória.

## Slide 9
Buoys: MD02 Albatros
  GPS
  GSM
  Temperature sensor
  Sends the GPS position every 2 minutes;
  Automatic upload on internet, ftp and Google Earth.
Drifters, containers and floating objects Field works in Estoril Coast
Notes: Na Costa do Estoril foram lançadas bóias que contém um cartão GPS, que regista a localização, e um cart~ºao GSM, que tranamite frequentemente a posição e temperatura da bóia.
Os dados são recebidos por um programa adequado, que os regista e grafica, e os transfere para um FTP, permitindo que estes sejam actualizados quase em tempo real, no GoogleEarth.

## Slide 10
Methodology
Before exercise:
    Model simulations, to choose the best start time and location for each release.
    Predict buoys location during each release.
    Test buoys, and communication tools:
      Buoys: SMS transmission, calls reception, GPS location.
      Automatic FTP upload, GoogleEarth actualization.
Drifters, containers and floating objects Field works in Estoril Coast
Notes: Antes de cada exercício de campo, eram efectuadas várias simulações com o MOHID, de forma a estudar os possiveis pontos e horas de lançamento. Eram estudados vários cenários tendo em conta diferentes ventos, e coeficientes de dispersão.
Analisando esses resultados eram definidos os vários pontos de lançamento, e anotada a rota que as bóias deveriam tomar.
O funcionamento das bóias era testado (verifcar se enviavam os SMS, se enviavam os com a frequência desejada, se respondiam às chamadas, e se estavam a dar as informações correctas (GPS, hora, temperatura).
A actualização dos dados no google Earth tb foi testada.

## Slide 11
Methodology
    During exercise:
    Release buoys on the planned point and time;
    Follow the buoys drift;
    Follow the buoys in real time with a notebook (results available on ftp/GoogleEarth)
    Measure wind data (velocity and direction);
    Pay attention of buoys position, fisher and transatlantic boats, proximity to bathing waters, and localized field conditions and phenomena, Rescue buoys if needed;
    If necessary run new model simulations to choose an alternative release point- results on 5/10 minutes.
Drifters, containers and floating objects Field works in Estoril Coast

## Slide 12
N/NW 7 knots
Windcoefficient
0.015
Calibration of model wind coefficients
Drifters, containers and floating objects Field works in Estoril Coast  Model Calibration
Notes: Wind Coefficiente: 0.015
Immediately after the release, the coefficient of 0 seems to be the best fit, however analysing
the evolution of the trajectory along time it is possible to see that coefficient 0.015 is the one
that best simulates the buoys drift trajectory.

## Slide 13
Wind: 2m/s
360º/360º
Validate local water properties dynamics
Drifters, containers and floating objects Field works in Estoril Coast  Model Calibration
Notes: During the exercise, the buoys followed an unexpected track, with a turn back circulation. For
this survey, the turbulent diffusion value that better represents this behaviour is the 0.02 for
VarvelHX, however, 0.03 also seems to be in good agreement with data, specially for the first
instants.

## Slide 14
Drifters, containers and floating objects Field works in Estoril Coast  Model Calibration
Validate local water properties dynamics
Notes: Photo of 27th August release, with visual difference between Tagus estuary water (on
the right), and Ocean water (on the left). To better visualization was drawned an orange line
identifying the “boundary”.
At the beginning, buoys were moving in a group, but with the influence of flood tide, two separated water masses from the estuary and from the ocean became clear and visible, and buoys started to drift exactly on the boundary of both water masses. Fresh water doesn’t mix with the ocean’s salt water, but has a tendency to lie on top of the salt water, because it is lighter. Buoys drift on the boundary of both waters can be explained by the differences in density between both water masses, generating a tidal convergence front which “trap” the buoys there. Thus, this is an example of the importance of the water density gradients in the buoys drift behaviour in Estoril Coast, which must be well represented in the modelling applications, in order to produce adequate drift simulations.
The survey in August 27th was also important to verify a small eddy usually represented by the model, and that has never been validated before.

## Slide 15
Validate local water properties dynamics
Buoys follow Tagus mouth residual plume
Drifters, containers and floating objects Field works in Estoril Coast  Model Calibration

## Slide 16
N/NW 7 knots
Windcoefficient
0.015
Atmospheric forcing MM5
Atmospheric forcing WRF
Field Measurements
Drifters, containers and floating objects Field works in Estoril Coast  Model Calibration
Different meteo inputs
Notes: model drift results were compared using atmospheric models with different spatial resolutions (MM5-9km, WRF 3 Km, and anemometer.
After this exercise, the high resolution WRF model was implemented fully operational, and results from this atmospheric model started to be used in all MOHID applications for this study area, improving MOHID results.
in‐situ measurements were also conducted inside the ship following the buoys, with a portable anemometer, allowing the validation of the WRF atmospheric model, and also to have access to a more realistic data source for the wind. In some exercises, the results derived with the in‐situ measurements revealed to be more accurate than with the
atmospheric model results.

## Slide 17
Wind: 2m/s
360º/360º
Validate model dispersion
Drifters, containers and floating objects Field works in Estoril Coast  Model Calibration
Notes: During the exercise, the buoys followed an unexpected track, with a turn back circulation. For
this survey, the turbulent diffusion value that better represents this behaviour is the 0.02 for
VarvelHX, however, 0.03 also seems to be in good agreement with data, specially for the first
instants.

## Slide 18
Main results and model developments
Validation of Drift MOHID applications in Galicia (Spain), Mondego, and Estoril Coast ;
Wind coefficient calibratiion;
Diffusion coefficients calibration;
Improve MOHID meteorological data input: MM5 (9km) > WRF (3Km);
Review of bathimetry data;
Helps to identify local and unique hydrodynamic and water properties phenomena.
MOHID model adapted to specify depth (from free surface) for drifter position.
Drifters, containers and floating objects Main results and model developments
Notes: Wind Coefficient calibration: 1-2% (0.015, 0.02)
A turbulent diffusion that depends linearly on the velocity absolute value with VARVELHX = 0.02 is promising.

## Slide 19
Work developed in the scope of several projects :
  Drifter;
  Arcopol;
  Porto Novo;
  ESOO;
Drifters, containers and floating objects
Tanks for your attention!
MOHID Workshop ARCOPOL- Lisbon, 13-10-2011
Notes: Wind Coefficient calibration: 1-2% (0.015, 0.02)
A turbulent diffusion that depends linearly on the velocity absolute value with VARVELHX = 0.02 is promising.